## Slide 1: Design and Implementation of a Microcontroller-Based Smart Sensor System
Course: Undergraduate Advanced Research Experience
Instructor: Dr. Jeong
By: Christopher Martin

## Slide 2: Project Overview
Goal: Detect occupancy and location using ultrasonic sensors
Support energy efficiency, automation, and smart homes
Phases:
  Phase 1: Single-node detection
  Phase 2: Multi-sensor wireless monitoring (Wi-Fi + Firebase)

## Slide 3: Motivation
Energy waste from lights/HVAC left on
Need for non-invasive, privacy-safe monitoring
Applications:
  Smart homes
  Healthcare monitoring
  Energy optimization

## Slide 4: System Architecture

## Slide 5: Hardware Components
Arduino Uno
3 × Ultrasonic Sensors (HC-SR04)
I2C LCD Display
Breadboard, jumper wires

## Slide 6: Software & Tools
Arduino IDE (Sensor reading + LCD + Serial JSON)
Python (Serial, Flask, Firebase, SMTP email)
Firebase Realtime Database (Cloud storage)
Chart.js + HTML Dashboard for real-time visualization

## Slide 7: Key Features
Location Estimation:“Front Left”, “Back Center” on LCD
Alerts:Stillness > 1 min → EmailObject very close (<10 cm) → Email
Data Visualization:Live dashboard with charts

## Slide 8: Arduino Implementation
Reads 3 ultrasonic sensors
Displays location on LCD
Sends JSON data over Serial
Example JSON:
{"S1": 123, "S2": 145, "S3": 134}

## Slide 9: Python Integration
Serial → Firebase → Dashboard
Email alerts using Mailtrap SMTP
Flask for real-time chart:

## Slide 10: Results
System tested for movement detection
Stillness detection accuracy: ±1 cm tolerance
Firebase logs verified
Dashboard updated every 2 seconds

## Slide 11: Future Improvements
Add ESP32 wireless nodes
Implement MQTT for scalability
Historical trend analysis on dashboard
Mobile app integration

## Slide 12: Conclusion
IoT + Embedded systems can enable smart monitoring
Affordable, privacy-preserving, real-time solution
Supports energy savings and automation